COMPILERS Instruction Selection
COMPILERS
Instruction Selection
hussein suleman
uct csc3003s 2008

---
Introduction
Introduction
IR expresses only one operation in each node.
MC performs several IR instructions in a single MC instruction.
  - e.g., fetch and add
MEM
BINOP
PLUS
e
CONST
i

---
Preliminaries
Preliminaries
Express each machine instruction as a fragment of an IR tree – “tree pattern”.
Instruction selection is then equivalent to tiling the tree with a minimal set of tree patterns.

---
Jouette Architecture 1/2
Jouette Architecture 1/2
Name
Effect
Trees
TEMP
ri
rj
+
rk
ADD
+
*
Note: All tiles on this page have an upward link like ADD
ri
rj
*
rk
MUL
ri
rj
-
rk
SUB
-
/
ri
rj
/
rk
DIV
+
+
CONST
ri
rj
+
c
ADDI
CONST
CONST
-
ri
rj
-
c
SUBI
CONST
MEM
MEM
MEM
MEM
ri
M[rj + c]
LOAD
+
+
CONST
CONST
CONST

---
Jouette Architecture 2/2
Jouette Architecture 2/2
Name
Effect
Trees
MOVE
MOVE
MOVE
MOVE
STORE
M[rj + c]
ri
MEM
MEM
MEM
MEM
+
+
CONST
CONST
CONST
MOVE
MOVEM
M[rj]
M[ri]
MEM
MEM

---
Instruction Selection
Instruction Selection
The concept of instruction selection is tiling.
Tiles are the set of tree patterns corresponding to legal machine instructions.
We want to cover the tree with non-overlapping tiles.
Note: We wont worry about which registers to use - yet.

---
Tiled Tree 1
Tiled Tree 1
MOVE
MEM
MEM
+
+
MEM
*
FP
CONST x
+
TEMP i
CONST 4
FP
CONST a
r1
LOAD
M[fp + a]
r2
r0
+
4
ADDI
r2
*
r3
r2
MUL
r1
+
r2
r1
ADD
r4
LOAD
M[fp + x]
Operation: a[i] = x
STORE
M[r1 + 0]
r4

---
Tiled Tree 2
Tiled Tree 2
MOVE
MEM
MEM
+
+
MEM
*
FP
CONST x
+
TEMP i
CONST 4
FP
CONST a
r1
LOAD
M[fp + a]
r2
r0
+
4
ADDI
r2
*
r3
r2
MUL
r1
+
r2
r1
ADD
r4
ADDI
fp + x
Operation: a[i] = x
MOVEM
M[r1]
M[r4]

---
Optimum and Optimal Tilings
Optimum and Optimal Tilings
Best tiling corresponds to least cost instruction sequence.
Each instruction is costed (somehow).
Optimum tiling
  - tiles sum to lowest possible value
Optimal tiling
  - no two adjacent tiles can be combined to a tile of lower cost
Note: Optimum tiling is Optimal, but not vice versa!

---
Maximal Munch Algorithm
Maximal Munch Algorithm
Start at the root.
Find the largest tile that fits.
Cover the root and possibly several other nodes with this tile.
Repeat for each subtree.
Generates instructions in reverse order.
If two tiles of equal size match the current node, choose either.

---
Maximal Munch Example
Maximal Munch Example
MEM
+
CONST 2
CONST 1
MEM is matched by LOAD
CONST (2) is matched by ADDI
Instructions emitted (in reverse order) are:
ADDI r1  r0 + 2
LOAD r2  M[r1 + 1]
Note: In Jouette, r0 is always zero!
+
CONST
MEM

---
Dynamic Programming Algorithm
Dynamic Programming Algorithm
Assign a cost to every node.
  - Sum of instruction costs of the best instruction sequence that can tile that subtree.
For each node n, proceeding bottom-up:
  - For each tile t of cost c that matches at n there will be zero or more subtrees, si, that correspond to the leaves (bottom edges) of the tile.
    - Cost of matching t is cost of t + sum of costs of all child trees of t
  - Assign tile with minimum cost to n.
Walk tree from root and emit instructions for assigned tiles.

---
Dynamic Programming Example 1/2
Dynamic Programming Example 1/2
MEM
+
CONST 2
CONST 1
CONST is only matched by an ADDI instruction with cost 1
The + node can be matched by
+
ADD cost 1 leaves 2 Total 3
+
ADDI cost 1 leaves 1 Total 2
CONST
+
ADDI cost 1 leaves 1 Total 2
CONST

---
Dynamic Programming Example 2/2
Dynamic Programming Example 2/2
The MEM node can be matched by
MEM
LOAD cost 1 leaves 2 Total 3
MEM
+
LOAD cost 1 leaves 1 Total 2
CONST
MEM
LOAD cost 1 leaves 1 Total 2
+
CONST
Instructions emitted (in reverse order, in second pass) are:
ADDI r1  r0 + 1
LOAD r2  M[r1 + 2]

---
Efficiency of Algorithms
Efficiency of Algorithms
Assume (on average):
  - T tiles
  - K non-leaf nodes in matching tile
  - Kp is largest number of nodes to check to find matching tile
  - Tp no of different tiles matching at each node
  - N nodes in tree
Cost of MM: O((Kp + Tp)N/K)
Cost of DP: O((Kp + Tp)N)
In both cases, with Kp, Tp, K constant
  - O(N)

---
Handling CISC Machine Code
Handling CISC Machine Code
Fewer registers:
  - E.g., Pentium has only 6 general registers
  - Allocate TEMPs and solve problem later!
Register use is restricted:
  - E.g., MUL on Pentium requires use of eax
  - Introduce additional LOAD/MOVE instructions to copy values.
Complex addressing modes:
  - E.g., Pentium allows ADD [ebp-8],ecx
  - Simple code generation still works, but is not as size-efficient, and can trash registers.

---
Implementation Issues
Implementation Issues
If registers are allocated after instruction selection, generated code must have “holes”.
  - Assembly code template: LOAD d0,s0
  - List of source registers: s0
  - List of destination registers: d0
    - Including registers trashed by instruction (e.g., return address and return value registers for CALLs)
Register allocation will then fill in the holes, by (simplistically) matching source and destination registers and eliminating redundancy.